## Slide 1
Update – November 2024
Current status: Non-compliant
Commentary
The plant remains non-compliant for suspended solids (90th percentile limit) and faecal coliforms (90-day geomean and 90th percentile limits). The current daily results for suspended solids are trending back into compliance by end of December for both the 90-day geomean and 90th percentile limits. Daily results for faecal coliforms show occasional spikes in results which is affecting the 90-day geomean and 90th percentile limits and continues to be investigated.
Discharges
There was one unconsented wet weather discharge via the short outfall on 15 November due to the reduced pumping capacity of the Inlet Pumping Station, whilst the riser pipe renewal project takes place (see items of significance).
Odour
There were two odour complaints in November. One relating to Moa Point, the other relating to the Southern Landfill site and Careys Gully Sludge Dewatering plant.
Items of significance:
​Clarifier #1 Renewal Project
Physical works have begun to replace the main bearing and renew structural elements on the final clarifier. With only two of the three clarifiers in operation, pumping capacity is reduced. Work is being carried out over the summer/autumn months when effluent flows are expected to be lower. The project is expected to be completed by mid-2025.
Inlet Pump Station (IPS) Project
Physical works for the third and final phase of the IPS project are progressing well and is on target for completion by March 2025. This involves replacing the remaining four of 10 riser pipes, along with four of the 10 submersible pumps, strengthening the IPS’s resilience for high rainfall events.
Moa Point Wastewater Treatment Plant performance

## Slide 2
Update – November 2024
Current status: Compliant
Commentary
The plant is compliant for effluent quality.
Discharges
No discharges in November.
Odour Complaints
No odour complaints in November.
Items of significance:
UV Performance Issues
Changes made to date have improved UV performance during high volume flows. Additional monitoring is in place to identify the intermittent fault, should it occur, and the system will continue to be closely monitored.
UV Backup Power Project
Physical works have begun to provide the plant with a dedicated generator for backup power supply aiming to ensure continuous UV treatment in events such as power outages. The project is expected to be completed by early 2025.
Porirua Wastewater Treatment Plant performance

## Slide 3
Update – November 2024
Current status: Non-compliant
Commentary:
The plant remains non-compliant for faecal coliforms (90-day geomean, 80th percentile limit).
Discharges:
There was one consented discharge of fully treated effluent to the Waiwhetu Stream on 15 November due to wet weather.
Odour Complaints
The plant received 60 odour complaints in November. On seven occasions GWRC deemed the odour Offensive and Objectionable.
Items of significance:
Increase in Odour
The increase in odour relates to mechanical failures with the sludge dryer and planned maintenance to the primary sedimentation tanks. The former resulted in biological process issues and solids buildup within the system. Work is ongoing to return the plant to normal operations with recent improvements to the process noted helping reduce the odour.
Infringement Notice issued
GWRC issued an Infringement in relation to the Biofilter Project Abatement for late delivery of documentation relating to the project. The relevant documents have since been updated and provided.
Seaview Wastewater Treatment Plant performance

## Slide 4
Update – November 2024
What has been completed:
Design for the milli-screening ducting replacement and air treatment for both milli-screen and dryer buildings are complete with an independent review underway.
What is currently in progress:
Independent review of stage 2 design will be completed in December
Implementation planning procurement strategy is progressing.
Odour scouting in the community continues.
Seaview Wastewater Treatment Plant performance – Odour Treatment

## Slide 5
Update – November 2024
Current status: Compliant
Commentary
The plant is compliant for effluent quality.
Discharges
No discharges in November.
Odour complaints
No odour complaints in November.
Items of significance:
No items of significance currently.
Western Wastewater Treatment Plant performance